## Slide 1
Fracturing Using Supercritical CO2 and Water – Application to Carbon Sequestration
Blessed Amoah
Integrated Core Characterization Center (IC3)
University of Oklahoma
CCUS Conference
October 4th, 2023
1

## Slide 2
Outline
Motivation
Experimental procedure
Results and discussion
  Breakdown pressure and acoustic emissions
  Hypocenter location of acoustic emissions
  Fracture dimensions
  Permeability of fracture
  Fracture morphology
Conclusions
Summary
Recommendation
2

## Slide 3
Motivation
  High injection pressure of CO2 :
  Increase the storage capacity of CO2
  Injection – induced fractures pose risk to CO2 containment
    Breakdown pressure is typically determined in a leak-off test (uses a water-based fluid)
Damen et al. 2006
3
Notes: Carbon Capture and Storage (CCS) is among the suite of technologies which can play an important role in meeting the climate goals.
95% of the estimated 280 MtCO2 to be stored in subsurface formations (IEA, 2022)
To safely sequester carbon dioxide in the subsurface CCS operators are required to inject CO2 below the formation breakdown pressure.
This precludes the creation of injection – induced fractures which poses the risk of CO2 leakage into freshwater aquifers and the atmosphere. With the creation of fractures, there is also an associated risk of induced seismicity which can be hazardous to the environment.
However, higher injection pressure allows to displace more formation brine, thus enhancing the effective storage capacity of the sequestration zone.
To optimize the injection pressure, mini-frac tests are typically conducted a drilling fluid that is water based and not gas-based to determine the formation breakdown pressure.
However, considering the significant dissimilarity in fluid properties between water – based fluid and supercritical CO2 (ScCO2) the breakdown pressure, failure mechanism and extent of damage resulting from the injection of these different fluids can vary.

## Slide 4
Objective
4
Investigate induced fractures risk during supercritical CO2 injection

## Slide 5
Experimental procedure
5
Sample | Gas filled porosity (%) | Permeability (md) | Mineralogy (wt%) |  | 
 |  |  | Quartz | Clay | Others
Tennessee sandstone (six cylindrical samples) | 6.5 | 0.015 | 84 | 11 | 5
Saturation
(2.5% KCl brine, 5000 psi) 72 hours
Measure P-wave velocity with azimuth
Fluid injection at 10 cc/min
Monitor acoustic emissions (16 sensors)
Pre fracturing characterization:
Permeability
Porosity
Mineralogy
Rock fracturing
(Water or scCO2)
Post fracturing characterization:
  Breakdown pressure
  Acoustic emissions
  Fracture dimensions
  Permeability
  Fracture morphology
4 in
5.2 in
Stresses (psi): σV= 1500, σh = 500, σH= 3000

## Slide 6
Experimental procedure
Axial Loading System
Confining vessel
Jacketed sample
Flat jacks
Acoustic
transducer
Jacket
Unjacketed sample
Jacketed sample
Triaxial Cell
6
Top of sample
Injection point
Steel tubing
Epoxy around the tubing
5.3”
4”
Bottom of sample
Borehole
Notes: I have two tests on core samples from the same block of Tennessee sandstone. One was with ScCO2 and the other with water
In terms of mineralogy, the samples are predominantly quartz rich with porosity of about 6.5%. The cores were saturated after which velocity measurement was taken on them. Afterwards I jacketed the samples and fixed 16 transducers on them. Only channel 14 is not working.
This is the profile of pressure and cumulative events generated during the water injection. There is a fast build up of pressure due to the incompressible nature of water until the sample failed which was accompanied with a sharp drop of pressure. Then the pressure stabilized at the minimum horizontal stress. More events at post propagation due to crushing of asperities on the fracture surfaces
Here is the profile for the ScCO2 injection. It appears different from that of water. There is a slow built up of pressure due to the compressible nature of ScCO2 until sample failure. Compared to the water injection profile, there is a slow drop in pressure after failure. We see more events at the propagation phase, and I attribute this to the expansion of ScCO2.

## Slide 7
Results and discussion
7

## Slide 8
Breakdown pressure and acoustic emissions
Water injection
scCO2 injection
8
Chart: Time (s)
Chart: Time (s)

## Slide 9
Acoustic emissions increased by a factor 4 using ScCO2.
Breakdown pressure and acoustic emissions
9
Chart: Number of acoustic emissions
| Water | ScCO2
Water | 856.3333
ScCO2 | 3435.3333
scCO2
Chart: Breakdown pressure (psi)
| Water | ScCO2
Water | 2246
ScCO2 | 1868.6667
scCO2
380 psi (16%)
Notes: The average breakdown pressure with ScCO2 is about 380 psi (16%) lower than with water.

## Slide 10
Hypocenter location: plan view
Located event Sensor
Chart: Y (mm)
| 0 | 0 | -35.92 | -35.92 | 35.92 | 35.92 | 35.92 | 35.92 | 0 | 0 | 0 | 0 | -35.92 | -35.92 | -32.5 | 32.5
Sensor | -50.8 | -50.8 | -35.92 | -35.92 | -35.92 | -35.92 | 35.92 | 35.92 | 50.8 | 50.8 | 50.8 | 50.8 | 35.92 | 35.92 | 0 | 0
Chart: Y (mm)
| 0 | 0 | -35.92 | -35.92 | 35.92 | 35.92 | 35.92 | 35.92 | 0 | 0 | 0 | 0 | -35.92 | -35.92 | -32.5 | 32.5
Sensor | -50.8 | -50.8 | -35.92 | -35.92 | -35.92 | -35.92 | 35.92 | 35.92 | 50.8 | 50.8 | 50.8 | 50.8 | 35.92 | 35.92 | 0 | 0
Chart: Y (mm)
| 0 | 0 | -35.92 | -35.92 | 35.92 | 35.92 | 35.92 | 35.92 | 0 | 0 | 0 | 0 | -35.92 | -35.92 | -32.5 | 32.5
Sensor | -50.8 | -50.8 | -35.92 | -35.92 | -35.92 | -35.92 | 35.92 | 35.92 | 50.8 | 50.8 | 50.8 | 50.8 | 35.92 | 35.92 | 0 | 0
Water injection
scCO2 injection
10
Notes: The wider distribution of events about the x axis for the ScCO2 fracturing experiment is due to:
  Intense microcracking
  Complexity of the velocity model

## Slide 11
Fracture dimensions
Water injection
scCO2 injection
11
Fracture
Bottom
Top
Bottom
Top
Right side view
Left side view
Right side view
Fracture
Fracture
No fracture
No fracture
σH
σh
Fracture
Fracture
σV
σH
σh
Left side view
Fracture
σV
σH
σh

## Slide 12
Gas permeability of fractured plugs
12
Helium gas
Dried state
1”
2”
Fracture
Plug
0.2” gap
1”
X
Y
Bore hole
Fracture
Chart: Confining pressure (psi)
| 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000
Native | 0.022 | 0.016 | 0.013 | 0.011 | 0.01 | 0.009 | 0.008 | 0.007
Post water fracturing | 15.741 | 5.761 | 3.292 | 2.155 | 1.514 | 1.119 | 0.858 | 0.675
Post ScCO2 fracturing | 193.86 | 79.984 | 42.441 | 26.229 | 17.602 | 12.459 | 8.991 | 6.631

## Slide 13
Fracture morphology
13
Courtesy: Mark Curtis
1“
Injection point
0.2” in gap
SEM study
X
Z
Disk for imaging
Fracture aperture
40 µm
Primary fracture
400µm
σH
Asperities
Secondary fracture
400µm
Clean fracture (without loose grain)
Aligned asperities
400µm
Wider fracture aperture
σH
400µm
200 µm
Secondary cracks
Mismatched asperities
400µm
Intense microcracking
Multiple loose grains
400µm
Water injection
scCO2 injection
Courtesy: Mark Curtis

## Slide 14
Our experiments with ScCO2 and water in Tennessee sandstone shows:
  The average breakdown pressure with ScCO2 is about 380 psi (16%) lower than with water.
  ScCO2 fracturing shows an increase by a factor of 4 in acoustic emissions
  Fractures created by ScCO2 are more complex (longer length, wider aperture, mismatched asperities and loose grains). Consequently, this leads to an increase in permeability of fractures by one order of magnitude.
Conclusions
Recommendation
Laboratory fracturing studies with CO2 on core samples to determine the exact breakdown pressure.
14
Summary
Formation breakdown will occur at a lower pressure with ScCO2 injection than the estimated breakdown pressure from leak-off test. Generated fractures can propagate long distances into the formation and can be more transmissive. Thus, these fractures can easily facilitate the migration of CO2 from the sequestration zone.
Thank you

## Slide 15
Acknowledgement
Advisors
Dr. Chandra Rai
Dr. Carl Sondergeld
Dr. Son Dang
Dr. Mark Curtis
Dr. Deepak Devegowda
IC3 Technical Assistants
Micaela Langevin
Gary Stowe
15

## Slide 16
Damen, K., Faaij, A.P.C., and Turkenburg, W.C. 2006. Health, Safety and Environmental Risks of Underground Co2 Storage-Overview of Mechanisms and Current Knowledge. Climatic Change.
References
16

## Slide 17
Back-up slides
17
Notes: Diffusion coefficient of

## Slide 18
Acoustic emissions increased by a factor 4 using ScCO2.
Breakdown pressure and acoustic emissions
18
Chart: Number of acoustic emissions
| Water | ScCO2
Water | 856.3333
ScCO2 | 3435.3333
ScCO2
Chart: Breakdown pressure (psi)
| Water | ScCO2
Water | 2246
ScCO2 | 1868.6667
ScCO2
380 psi (16%)
ScCO2 viscosity: 15 times lower than water viscosity (Deng. et al. 2021)
Notes: The average breakdown pressure with ScCO2 is about 380 psi (16%) lower than with water.

## Slide 19
Lv et al. 2019)
Notes: I have two tests on core samples from the same block of Tennessee sandstone. One was with ScCO2 and the other with water
In terms of mineralogy, the samples are predominantly quartz rich with porosity of about 6.5%. The cores were saturated after which velocity measurement was taken on them. Afterwards I jacketed the samples and fixed 16 transducers on them. Only channel 14 is not working.
This is the profile of pressure and cumulative events generated during the water injection. There is a fast build up of pressure due to the incompressible nature of water until the sample failed which was accompanied with a sharp drop of pressure. Then the pressure stabilized at the minimum horizontal stress. More events at post propagation due to crushing of asperities on the fracture surfaces
Here is the profile for the ScCO2 injection. It appears different from that of water. There is a slow built up of pressure due to the compressible nature of ScCO2 until sample failure. Compared to the water injection profile, there is a slow drop in pressure after failure. We see more events at the propagation phase, and I attribute this to the expansion of ScCO2.

## Slide 20
Viscosity and diffusion coefficient of ScCO2
Viscosity: 0.05 – 0.07 cp @ 310K and 11.8 MPa
Viscosity: 20 – 15 times lower than that of water
Deng et al., 2021
Diffusion/leak off rate of CO2 @ 333.15 – 373.15 K, 10-25 MPa, 50 mD = 0.9 – 18.5 * 10-4 cm3/s (Lv et al., 2019)
Injection/pressure build up rate: 10 cm3/s
Compressibility of CO2 = 10-9 – 10-8 Pa-1 which is 1 – 2 order of magnitude greater than that of water
Notes: Diffusion coefficient of